Title	: Study report on mapping the interface requirement of GISFI Lightweight IoT architecture with OneM2M architecture

Company	: NEC

Contact information: 	Sivabalan.arumugam@necindia.in, anand@bq.jp.nec.com

Purpose		: Discussion and approval

Doc number	: GISFI_IoT_201403445

Meeting		: GISFI#16, Delhi, India, 10th to 12th March 2014

# Abstract

This document discusses the detailed mapping of Health care requirements of various interfaces present in GISFI IoT Lightweight architecture with other SDOs M2M/IoT/MTC architectures reference points. Section 2 describe the import Health care use requirement derived from GISFI IoT Health care usecase documents includes i. GISFI_IoT_201206226:Usecase Interface Requirements Technical Report, ii. GISFI_IoT_201203179:Internet of Things - mHealth Use Cases, iii. GISFI_IOT_201206222:Healthcare Service Delivery mechanism  based on Generic IOT Framework  and OneM2M health usecase document  oneM2M-TR-0001-UseCase: oneM2M Use cases collection.

# IoT/M2M General requirements

## GISFI IoT Health care requirements

There are different medical sensors devices like ECG, Oxymeter, Fat-analyzer, Blood-pressure etc. to generate data. They are mainly resource constrained devices. The medical sensor devices apply various syntax and semantics while exchanging the information.

The medical gateway considered as mobile phone which communicates with these medical devices is mainly battery powered. Gateway aggregates the sensor data and publishes this information over the Internet, to the service platform. This gateway also supports the reverse message flow like controlling the medical sensor device by the application for setting a specific parameter remotely. The application supports real-time video conference over the service platform between the doctor and the patients for remote consultation.

In general the sensor data contain sensitive data or private healthcare information of the patient.

General requirements for the ‘IoT-Medical-system’ are stated below.

- Device discovery, registration, capability negotiation of the medical sensors

- Interoperability w.r.t received sensor data format from the various medical devices obeying different medical device standards, even of the same category.

- Support broadcasting to upgrade the medical devices, maintaining the resource optimization aspect.

- Communication protocols for exchanging the healthcare information should use the power and bandwidth of the sensing device and mHelath-gateway/mobile phone in an optimized manner.

- Application protocols should support event based notification mechanism/ alarm generation from the medical devices, supports both publish-subscribe and request-response.

- Ensure reliability while transmitting critical life events.

- Real time supports of the critical life events

- Need a secure communication channel

- Support handling of the priority messages in case of emergency services

- Requires user authentication

- Requires privacy preservation as per the user choice on their personal healthcare information.

- Requires supporting multimedia streaming with good QoS.

The bold points are explicitly required for mHealth case.

## OneM2M Health care requirements

- The M2M system shall be capable of supporting gateway nodes that are capable of transporting sensor measurements to back end servers.

- Whenever a healthcare sensor has measurement data available, it shall be possible for the sensor to send a request to the local healthcare gateway to transport new measurement data to the backend server.

- The local healthcare gateway needs to be capable to buffer incoming requests from the healthcare sensor for transporting data to the backend server and support forwarding them at a later time – which could potentially be a very long time in the order of hours, days or even more – depending on cellular network availability, cellular network utilization policies, device constraints

- The local healthcare gateway needs to be capable of accepting parameters with incoming requests from the healthcare sensor source which define a QoS policy for initiating the delivery of the sensor measurements or parameters for categorizing sensor measurements into different levels of priority/QoS.

- The local healthcare gateway needs to be able to concurrently process multiple streams of data from different sources with awareness for the stream processing requirements for each of the streams. The local healthcare gateway needs to address the QoS policy of one or more concurrent streams while taking into account network constraints such as available link performance and network cost. The local healthcare gateway needs to adapt to dynamic variations in the available link performance or network communication cost or network availability to deliver one or more data streams concurrently

- The local healthcare gateway needs to be capable of receiving policies which express cellular network utilization constraints and which shall govern the decision making in the gateway when initiating connectivity over cellular networks.

- The local healthcare gateway needs to be capable to trigger connections to the cellular network in line with the parameters given by the request to transport data and in line with configured policies regarding utilization of the cellular network

- The M2M system shall be capable of supporting a mechanism to allow applications (residing on the local gateway, on the backend server or on the sensor itself) to subscribe to data of interest and get notifications on changes or availability of that data.

- The M2M system needs to be able to allow access to data that is being transported or buffered only to authenticated and authorized applications

- The M2M system shall support transport of data from the backend server to the cellular healthcare gateway.

- The M2M system shall support of triggering a cellular connection to the local healthcare gateway in case the gateway supports such functionality.

- Subscriber-specific filters can be set up at the healthcare service enterprise backend server so that each subscriber can be notified only when information/events relevant to the subscriber are available/occur.

- The M2M system shall be able to support a wakeup trigger (aka "shoulder-tap") mechanism (such as using SMS or alternate mechanisms) to wake up the gateway. The gateway can subsequently establish a network connection and query the enterprise backend server for additional information, and the enterprise backend server may then respond with adequate information to enable further processing of its request.

- When some of the components of M2M System are not available (e.g. WAN connection lost), the M2M System shall be able to support the normal operation of components of the M2M System that are available.

- When some of the components of M2M System are not available (e.g. WAN connection lost), the M2M System shall be able to support the confidentiality and the integrity of data between authorized components of the M2M System that are available.

# Existing Functional Entities: ATIS, ETSI, TIA, GISFI

This section provides a comparative analysis of existing ATIS M2M, ETSI M2M, TIA TR-50, and GISFI IoT, functional architectural entities. Table 1 provides a comparative matrix of the functional architectural entities supported by each architecture

Table 1 TIA, ATIS, ETSI, and GISFI M2M/IoT Functional Entity Comparative Matrix

| Functional Entity | TIA TR-50 | ATIS | ETSI M2M | GISFI IoT |
| --- | --- | --- | --- | --- |
| M2M Service Capability hosted in the network domain | Yes Server Container | Yes Service Capabilities | Yes Network Service Capability Layer (NSCL) | Yes Service Capabilities |
| M2M Service Capability hosted on an intermediary node | Yes PoA Container | No | Yes Gateway Service Capability Layer (GSCL) | Yes Through Gateways |
| M2M Service Capability hosted on an M2M Device | Yes PoA Container | No | Yes Device Service Capability Layer (DSCL) | No |
| Applications in the network domain | Yes home applications | Yes Applications | Yes Network Applications (NA) | Yes |
| Applications in the intermediary node | Yes Node Application | No | Yes Gateway Application (GA) | No |
| Applications in the M2M Device | Yes PoA Application | No | Yes Device Application (DA) | No |
| M2M Network | Yes Server | Yes Network Service Functions | Yes Network Domain | Yes |
| M2M intermediary node | Yes PoA Device | No | Yes M2M Gateway | No |
| M2M Device | Yes PoA Device | Yes Device | Yes Device with Service Capabilities (D) Device without Service Capabilities (D') Legacy non-ETSI Device (d) | No device to device interface is out of scope |
| AAA Server | Yes AAA-SD | No | Yes M2M Authentication Server (MAS), M2M Service Bootstrap function (MSBF) | No |

# Mapping of reference point among TIA. ETSI, ATIS, GISFI

This section provides a comparative analysis of existing TIA TR-50, ETSI M2M, ATIS M2M and GISFI IoT, architectural reference points. Figure 1 shows the reference points from each source consolidated into a single functional architecture. Table 2 provides a comparative matrix of the reference points supported by each architecture.

Figure 1: TIA, ATIS, ETSI, and GISFI M2M/IoT Reference Point Analysis

Table 2: TIA, ETSI, ATIS, and 3GPP Reference Point Analysis for M2M

| Reference Point/Interface Description | Corresponding Reference Point |
| --- | --- |
|  | TIA | ETSI | ATIS | 3GPP | GISFI |
| M2M Device Application ↔ M2M Device Application | B5 |  |  |  | I2 |
| M2M Gateway Application ↔ M2M Gateway Application | B4 |  |  |  |  |
| M2M Device Application ↔ M2M Gateway Application | B3 |  |  |  |  |
| M2M Device Application ↔ M2M Network Application | B2 |  |  |  |  |
| M2M Gateway Application ↔ M2M Network Application | B1 |  |  |  |  |
| M2M Device Application ↔ M2M Device | B9 |  |  |  |  |
| M2M Gateway Application ↔ M2M Device | B3' |  |  |  |  |
| M2M Network Application ↔ M2M Device | B2' |  | * |  |  |
| M2M Network Application ↔ Access/Core Network Provider |  |  |  | Gi/Sgi |  |
| M2M Device Application ↔ M2M Device Service Layer |  | dIa |  |  | I1 |
| M2M Device Application ↔ M2M Gateway Service Layer |  | dIa |  |  | I1 |
| M2M Gateway Application ↔ M2M Device Service Layer | B8 |  |  |  |  |
| M2M Gateway Application ↔ M2M Gateway Service Layer |  | dIa |  |  | I1 |
| M2M Network Application ↔ M2M Device Service Layer | B7 |  |  |  |  |
| M2M Network Application ↔ M2M Gateway Service Layer | B6 |  |  |  |  |
| M2M Network Application ↔ M2M Network Service Layer |  | mIa | ASP IF |  | I3 |
| M2M Device Service Layer ↔ M2M Network Service Layer |  | mId |  |  | I2 |
| M2M Gateway Service Layer ↔ M2M Network Service Layer |  | mId |  |  | I2 |
| M2M Network Service Layer ↔ M2M Network Service Layer |  | mIm |  |  |  |
| M2M Network Service Layer ↔ M2M Device |  |  | * |  |  |
| M2M Network Service Layer ↔ Access/Core Network Provider |  |  | MSP IF | TSP |  |
| M2M Device ↔ M2M Device | B5' |  |  |  |  |
| M2M Device ↔ Access/Core Network Provider |  |  | NW IF |  |  |
| M2M Network Application ↔ AAA Server | A1 |  |  |  |  |
| M2M Gateway Application ↔ AAA Server | A2 |  |  |  |  |
| M2M Device Application ↔ AAA Server | A3 |  |  |  |  |
| M2M Device ↔ AAA Server | A3' |  |  |  |  |
| M2M Network Service Layer ↔ AAA Server |  | MAS/ MSBF |  |  |  |

# Conclusion

The present document offers an overview and summary of the most current standards activity related to M2M, with a goal of providing a common understanding of existing M2M Architectural approaches. The present document may be used to facilitate future normative work resulting in GISFI Technical Specifications

# Reference

- GISFI_IoT_201206226:Usecase Interface Requirements Technical Report

- GISFI_IoT_201203179:Internet of Things - mHealth Use Cases.

- GISFI_IOT_201206222:Healthcare Service Delivery mechanism based on Generic IOT Framework

- OneM2M health usecase document  oneM2M-TR-0001-UseCase: oneM2M Use cases collection.

- ATIS Machine to Machine (M2M) Committee

- ETSI Machine to Machine (M2M) Committee

- TIA TR-50 - M2M: "Smart Device Communications"

- oneM2M-TR-0003-Architecture_Analysis_Part_2-V-0.5.0: Architecture Analysis - Part 2: Study for the merging of architectures proposed for consideration by oneM2M